Computer Systems: Network Programming (Sockets)
David Marchant
Based on slides by Randal E. Bryant and David R. O’Halloran, with alterations by Vivek Shah

---
A Client-Server Transaction
A Client-Server Transaction
Most network applications are based on the client-server model:
  - A server process and one or more client processes
  - Server manages some resource
  - Server provides service by manipulating resource for clients
  - Server activated by request from client (vending machine analogy)
Client
process
Server
process
Resource
4. Client
handles
response
Note: clients and servers are processes running on hosts
(can be the same or different hosts)
1. Client sends request
3. Server sends response
2. Server
handles
request

---
Hardware Organization of a Network Host
Hardware Organization of a Network Host
CPU chip
register file
ALU
system bus
memory bus
main
memory
MI
I/O
bridge
Expansion slots
I/O bus
USB
controller
network
adapter
graphics
adapter
disk
controller
mouse
keyboard
monitor
disk
network

---
Global IP Internet (upper case)
Global IP Internet (upper case)
Most famous example of an internet
Based on the TCP/IP protocol family
  - IP (Internet Protocol) :
    - Provides basic naming scheme and unreliable delivery capability of packets (datagrams) from host-to-host
  - UDP (Unreliable Datagram Protocol)
    - Uses IP to provide unreliable datagram delivery from
      process-to-process
  - TCP (Transmission Control Protocol)
    - Uses IP to provide reliable byte streams from process-to-process over connections
Accessed via a mix of Unix file I/O and functions from the sockets interface

---
A Programmer’s View of the Internet
A Programmer’s View of the Internet
1. Hosts are mapped to a set of 32-bit IP addresses
  1. 128.2.203.179
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  1. 128.2.217.3 is mapped to www.cs.cmu.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

---
Aside: IPv4 and IPv6
Aside: IPv4 and IPv6
The original Internet Protocol, with its 32-bit addresses, is known as Internet Protocol Version 4 (IPv4)
1996: Internet Engineering Task Force (IETF) introduced Internet Protocol Version 6 (IPv6) with 128-bit addresses
  - Intended as the successor to IPv4
- As of 2021, majority of Internet traffic still carried by IPv4
  - Only 30-35% of users access Google services using IPv6.
We will focus on IPv4, but will show you how to write networking code that is protocol-independent.

---
(1) IP Addresses
IP Addresses
32-bit IP addresses are stored in an IP address struct
  - IP addresses are always stored in memory in network byte order (big-endian byte order)
  - True in general for any integer transferred in a packet header from one machine to another.
    - E.g., the port number used to identify an Internet connection.
/* Internet address structure */
struct in_addr {
    uint32_t s_addr; /* network byte order (big-endian) */
};

---
Dotted Decimal Notation
Dotted Decimal Notation
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    - IP address: 0x8002C2F2 = 128.2.194.242
- Use inet_ntop, inet_pton functions for converting between dotted decimal notation and IP addresses
  - Use htonl, htons, ntohl and ntohs functions for network byte order conversions
- Use getaddrinfo and getnameinfo functions (described later) to convert between IP addresses and dotted decimal format.

---
(3) Internet Connections
Internet Connections
Clients and servers communicate by sending streams of bytes over connections. Each connection is:
  - Point-to-point: connects a pair of processes.
  - Full-duplex: data can flow in both directions at the same time,
  - Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.
- A socket is an endpoint of a connection
  - Socket address is an IPaddress:port pair
- A port is a 16-bit integer that identifies a process:
  - Ephemeral port: Assigned automatically by client kernel when client makes a connection request.
  - Well-known port: Associated with some service provided by a server (e.g., port 80 is associated with Web servers)

---
Well-known Ports and Service Names
Well-known Ports and Service Names
Popular services have permanently assigned well-known ports and corresponding well-known service names:
  - echo server: 7/echo
  - ssh servers: 22/ssh
  - email server: 25/smtp
  - Web servers: 80/http
Mappings between well-known ports and service names is contained in the file /etc/services on each Linux machine.

---
Sockets Interface
Set of system-level functions used in conjunction with Unix I/O to build network applications.
Created in the early 80’s as part of the original Berkeley distribution of Unix that contained an early version of the Internet protocols.
Available on all modern systems
  - Unix variants, Windows, OS X, IOS, Android, ARM

---
Sockets
Sockets
What is a socket?
  - To the kernel, a socket is an endpoint of communication
  - To an application, a socket is a file descriptor that lets the application read/write from/to the network
    - Remember: All Unix I/O devices, including networks, are modeled as files
- Clients and servers communicate with each other by reading from and writing to socket descriptors
The main distinction between regular file I/O and socket I/O is how the application “opens” the socket descriptors
Client
Server
clientfd
serverfd

---
Socket Address Structures_clipboard0
Socket Address Structures
Generic socket address:
  - For address arguments to connect, bind, and accept
  - Necessary only because C did not have generic (void *) pointers when the sockets interface was designed
  - For casting convenience, we adopt the Stevens convention:
     typedef struct sockaddr SA;
struct sockaddr {
  uint16_t sa_family; /* Protocol family */
  char sa_data[14]; /* Address data. */
};
sa_family
Family Specific

---
Socket Address Structures
Socket Address Structures
Internet (IPv4) specific socket address:
  - Must cast (struct sockaddr_in *) to (struct sockaddr *) for functions that take socket address arguments.
struct sockaddr_in {
  uint16_t sin_family; /* Protocol family (always AF_INET) */
  uint16_t sin_port; /* Port num in network byte order */
  struct in_addr sin_addr; /* IP addr in network byte order */
  unsigned char sin_zero[8]; /* Pad to sizeof(struct sockaddr) */
};
sin_addr
sin_port
0
0
0
0
0
0
0
0
AF_INET
sa_family
sin_family
Family Specific

---
Host and Service Conversion: getaddrinfo_clipboard0
Host and Service Conversion: getaddrinfo
getaddrinfo is the modern way to convert string representations of hostnames, host addresses, ports, and service names to socket address structures.
  - Replaces obsolete gethostbyname and getservbyname funcs.
- Advantages:
  - Reentrant (can be safely used by threaded programs).
  - Allows us to write portable protocol-independent code
    - Works with both IPv4 and IPv6
- Disadvantages
  - Somewhat complex
  - Fortunately, a small number of usage patterns suffice in most cases.

---
Host and Service Conversion: getaddrinfo
Host and Service Conversion: getaddrinfo
- Given host and service, getaddrinfo returns result that points to a linked list of addrinfo structs, each of which points to a corresponding socket address struct, and which contains arguments for the sockets interface functions.
- Helper functions:
  - freeadderinfo frees the entire linked list.
  - gai_strerror converts error code to an error message.
int getaddrinfo(const char *host, /* Hostname or address */
        const char *service, /* Port or service name */
        const struct addrinfo *hints,/* Input parameters */
        struct addrinfo **result); /* Output linked list */
void freeaddrinfo(struct addrinfo *result); /* Free linked list */
const char *gai_strerror(int errcode); /* Return error msg */

---
Do-it-yourself Recap: System-level I/O
Do-it-yourself Recap: System-level I/O
- What is the difference between the Unix I/O and the book’s robust I/O APIs?
- When can short counts be returned by I/O functions? Why?
- What did each of the following functions do?
- ssize_t rio_writen(int fd, void *usrbuf, size_t n);
- ssize_t rio_readlineb(rio_t *rp, void *usrbuf, size_t maxlen);
- ssize_t rio_readnb(rio_t *rp, void *usrbuf, size_t n);

---
Socket Programming Example
Socket Programming Example
- Echo server and client
- Server
  - Accepts connection request
  - Repeats back lines as they are typed
- Client
  - Requests connection to server
  - Repeatedly:
    - Read line from terminal
    - Send to server
    - Read reply from server
    - Print line to terminal

---
Echo Client: Main Routine
#include "csapp.h"
int main(int argc, char **argv)
{
    int clientfd;
    char *host, *port, buf[MAXLINE];
    rio_t rio;
    host = argv[1];
    port = argv[2];
    clientfd = Open_clientfd(host, port);
    Rio_readinitb(&rio, clientfd);
    while (Fgets(buf, MAXLINE, stdin) != NULL) {
 Rio_writen(clientfd, buf, strlen(buf));
 Rio_readlineb(&rio, buf, MAXLINE);
 Fputs(buf, stdout);
    }
    Close(clientfd);
    exit(0);
}
echoclient.c

---
Iterative Echo Server: Main Routine
#include "csapp.h”
void echo(int connfd);
int main(int argc, char **argv)
{
    int listenfd, connfd;
    socklen_t clientlen;
    struct sockaddr_storage clientaddr; /* Enough room for any addr */
    char client_hostname[MAXLINE], client_port[MAXLINE];
    listenfd = Open_listenfd(argv[1]);
    while (1) {
 clientlen = sizeof(struct sockaddr_storage); /* Important! */
 connfd = Accept(listenfd, (SA *)&clientaddr, &clientlen);
 Getnameinfo((SA *) &clientaddr, clientlen,
        client_hostname, MAXLINE, client_port, MAXLINE, 0);
 printf("Connected to (%s, %s)\n", client_hostname, client_port);
 echo(connfd);
 Close(connfd);
    }
    exit(0);
}
echoserveri.c

---
Echo Server: echo function
The server uses RIO to read and echo text lines until EOF (end-of-file) condition is encountered.
  - EOF condition caused by client calling close(clientfd)
void echo(int connfd)
{
    size_t n;
    char buf[MAXLINE];
    rio_t rio;
    Rio_readinitb(&rio, connfd);
    while((n = Rio_readlineb(&rio, buf, MAXLINE)) != 0) {
        printf("server received %d bytes\n", (int)n);
Rio_writen(connfd, buf, n);
    }
}
echo.c

---
Echo
Server
+ Client
Structure_clipboard0
2. Start client
1. Start server
Server
Client
Echo
Server
+ Client
Structure
open_clientfd
open_listenfd
Connection
request
Await connection
request from client
accept
3. Exchange
data
4. Disconnect client
5. Drop client
Client / Server
Session
socket read
socket write
socket read
terminal write
terminal read
socket write
socket read
close
close
EOF

---
Echo
Server
+ Client
Structure
2. Start client
1. Start server
Server
Client
Echo
Server
+ Client
Structure
open_clientfd
open_listenfd
Connection
request
Await connection
request from client
accept
3. Exchange
data
4. Disconnect client
5. Drop client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
fputs
fgets
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Interface
Sockets Interface
Client
Server
getaddrinfo
getaddrinfo
socket
socket
open_listenfd
open_clientfd
bind
listen
Connection
request
connect
accept
Await connection
request from
next client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Interface: socket
Sockets Interface: socket
Clients and servers use the socket function to create a socket descriptor:
Example:
Protocol specific! Best practice is to use getaddrinfo to generate the parameters automatically, so that code is protocol independent.
int socket(int domain, int type, int protocol)
int clientfd = socket(AF_INET, SOCK_STREAM, 0);
Indicates that we are using 32-bit IPV4 addresses
Indicates that the socket will be the end point of a connection

---
Sockets Interface
Client
Server
getaddrinfo
getaddrinfo
socket
socket
open_listenfd
open_clientfd
bind
listen
Connection
request
connect
accept
Await connection
request from
next client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Interface: bind
Sockets Interface: bind
A server uses bind to ask the kernel to associate the server’s socket address with a socket descriptor:
      Recall: typedef struct sockaddr SA;
- Process can read bytes that arrive on the connection whose endpoint is addr by reading from descriptor sockfd
- Similarly, writes to sockfd are transferred along connection whose endpoint is addr
Best practice is to use getaddrinfo to supply the arguments addr and addrlen.
int bind(int sockfd, SA *addr, socklen_t addrlen);

---
Sockets Interface
Client
Server
getaddrinfo
getaddrinfo
socket
socket
open_listenfd
open_clientfd
bind
listen
Connection
request
connect
accept
Await connection
request from
next client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Interface: listen
Sockets Interface: listen
- By default, kernel assumes that descriptor from socket function is an active socket that will be on the client end of a connection.
- A server calls the listen function to tell the kernel that a descriptor will be used by a server rather than a client:
Converts sockfd from an active socket to a listening socket that can accept connection requests from clients.
backlog is a hint about the number of outstanding connection requests that the kernel should queue up before starting to refuse requests.
int listen(int sockfd, int backlog);

---
Sockets Interface
Client
Server
getaddrinfo
getaddrinfo
socket
socket
open_listenfd
open_clientfd
bind
listen
Connection
request
connect
accept
Await connection
request from
next client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Interface: accept
Sockets Interface: accept
Servers wait for connection requests from clients by calling accept:
Waits for connection request to arrive on the connection bound to listenfd, then fills in client’s socket address in addr and size of the socket address in addrlen.
Returns a connected descriptor that can be used to communicate with the client via Unix I/O routines.
int accept(int listenfd, SA *addr, int *addrlen);

---
Sockets Interface
Client
Server
getaddrinfo
getaddrinfo
socket
socket
open_listenfd
open_clientfd
bind
listen
Connection
request
connect
accept
Await connection
request from
next client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Interface: connect
Sockets Interface: connect
A client establishes a connection with a server by calling connect:
Attempts to establish a connection with server at socket address addr
  - If successful, then clientfd is now ready for reading and writing.
  - Resulting connection is characterized by socket pair
(x:y, addr.sin_addr:addr.sin_port)
    - x is client address
    - y is ephemeral port that uniquely identifies client process on client host
Best practice is to use getaddrinfo to supply the arguments addr and addrlen.
int connect(int clientfd, SA *addr, socklen_t addrlen);

---
accept Illustrated
accept Illustrated
listenfd(3)
1. Server blocks in accept, waiting for connection request on listening descriptor listenfd
Client
Server
clientfd
Connection
request
listenfd(3)
2. Client makes connection request by calling and blocking in connect
Client
Server
clientfd
listenfd(3)
3. Server returns connfd from accept. Client returns from connect. Connection is now established between clientfd and connfd
Client
Server
clientfd
connfd(4)

---
Connected vs. Listening Descriptors
Connected vs. Listening Descriptors
Listening descriptor
  - End point for client connection requests
  - Created once and exists for lifetime of the server
- Connected descriptor
  - End point of the connection between client and server
  - A new descriptor is created each time the server accepts a connection request from a client
  - Exists only as long as it takes to service client
- Why the distinction?
  - Allows for concurrent servers that can communicate over many client connections simultaneously
    - E.g., Each time we receive a new request, we fork a child to handle the request

---
Sockets Interface
Client
Server
getaddrinfo
getaddrinfo
socket
socket
open_listenfd
open_clientfd
bind
listen
Connection
request
connect
accept
Await connection
request from
next client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Helper: open_clientfd
Sockets Helper: open_clientfd
Establish a connection with a server
int open_clientfd(char *hostname, char *port) {
  int clientfd;
  struct addrinfo hints, *listp, *p;
  /* Get a list of potential server addresses */
  memset(&hints, 0, sizeof(struct addrinfo));
  hints.ai_socktype = SOCK_STREAM; /* Open a connection */
  hints.ai_flags = AI_NUMERICSERV; /* …using numeric port arg. */
  hints.ai_flags |= AI_ADDRCONFIG; /* Recommended for connections */
  Getaddrinfo(hostname, port, &hints, &listp);
csapp.c

---
Sockets Helper: open_clientfd (cont)
Sockets Helper: open_clientfd (cont)
    /* Walk the list for one that we can successfully connect to */
    for (p = listp; p; p = p->ai_next) {
        /* Create a socket descriptor */
        if ((clientfd = socket(p->ai_family, p->ai_socktype,
        p->ai_protocol)) < 0)
        continue; /* Socket failed, try the next */
        /* Connect to the server */
        if (connect(clientfd, p->ai_addr, p->ai_addrlen) != -1)
        break; /* Success */
        Close(clientfd); /* Connect failed, try another */
    }
    /* Clean up */
    Freeaddrinfo(listp);
    if (!p) /* All connects failed */
        return -1;
    else /* The last connect succeeded */
        return clientfd;
}
csapp.c

---
Sockets Interface
Client
Server
getaddrinfo
getaddrinfo
socket
socket
open_listenfd
open_clientfd
bind
listen
Connection
request
connect
accept
Await connection
request from
next client
Client / Server
Session
rio_readlineb
rio_writen
rio_readlineb
rio_writen
rio_readlineb
close
close
EOF

---
Sockets Helper: open_listenfd
Sockets Helper: open_listenfd
Create a listening descriptor that can be used to accept connection requests from clients.
 int open_listenfd(char *port)
{
    struct addrinfo hints, *listp, *p;
    int listenfd, optval=1;
    /* Get a list of potential server addresses */
    memset(&hints, 0, sizeof(struct addrinfo));
    hints.ai_socktype = SOCK_STREAM; /* Accept connect. */
    hints.ai_flags = AI_PASSIVE | AI_ADDRCONFIG; /* …on any IP addr */
    hints.ai_flags |= AI_NUMERICSERV; /* …using port no. */
    Getaddrinfo(NULL, port, &hints, &listp);
csapp.c

---
Sockets Helper: open_listenfd (cont)
Sockets Helper: open_listenfd (cont)
    /* Walk the list for one that we can bind to */
    for (p = listp; p; p = p->ai_next) {
        /* Create a socket descriptor */
        if ((listenfd = socket(p->ai_family, p->ai_socktype,
        p->ai_protocol)) < 0)
        continue; /* Socket failed, try the next */
        /* Eliminates "Address already in use" error from bind */
        Setsockopt(listenfd, SOL_SOCKET, SO_REUSEADDR,
        (const void *)&optval , sizeof(int));
        /* Bind the descriptor to the address */
        if (bind(listenfd, p->ai_addr, p->ai_addrlen) == 0)
        break; /* Success */
        Close(listenfd); /* Bind failed, try the next */
    }
csapp.c

---
Sockets Helper: open_listenfd (cont)
    /* Walk the list for one that we can bind to */
    for (p = listp; p; p = p->ai_next) {
        /* Create a socket descriptor */
        if ((listenfd = socket(p->ai_family, p->ai_socktype,
        p->ai_protocol)) < 0)
        continue; /* Socket failed, try the next */
        /* Eliminates "Address already in use" error from bind */
        Setsockopt(listenfd, SOL_SOCKET, SO_REUSEADDR,
        (const void *)&optval , sizeof(int));
        /* Bind the descriptor to the address */
        if (bind(listenfd, p->ai_addr, p->ai_addrlen) == 0)
        break; /* Success */
        Close(listenfd); /* Bind failed, try the next */
    }
csapp.c

---
Echo Client: Main Routine
Echo Client: Main Routine
#include "csapp.h"
int main(int argc, char **argv)
{
    int clientfd;
    char *host, *port, buf[MAXLINE];
    rio_t rio;
    host = argv[1];
    port = argv[2];
    clientfd = Open_clientfd(host, port);
    Rio_readinitb(&rio, clientfd);
    while (Fgets(buf, MAXLINE, stdin) != NULL) {
 Rio_writen(clientfd, buf, strlen(buf));
 Rio_readlineb(&rio, buf, MAXLINE);
 Fputs(buf, stdout);
    }
    Close(clientfd);
    exit(0);
}
echoclient.c

---
Iterative Echo Server: Main Routine
Iterative Echo Server: Main Routine
#include "csapp.h”
void echo(int connfd);
int main(int argc, char **argv)
{
    int listenfd, connfd;
    socklen_t clientlen;
    struct sockaddr_storage clientaddr; /* Enough room for any addr */
    char client_hostname[MAXLINE], client_port[MAXLINE];
    listenfd = Open_listenfd(argv[1]);
    while (1) {
 clientlen = sizeof(struct sockaddr_storage); /* Important! */
 connfd = Accept(listenfd, (SA *)&clientaddr, &clientlen);
 Getnameinfo((SA *) &clientaddr, clientlen,
        client_hostname, MAXLINE, client_port, MAXLINE, 0);
 printf("Connected to (%s, %s)\n", client_hostname, client_port);
 echo(connfd);
 Close(connfd);
    }
    exit(0);
}
echoserveri.c

---
Echo Server: echo function
Echo Server: echo function
The server uses RIO to read and echo text lines until EOF (end-of-file) condition is encountered.
  - EOF condition caused by client calling close(clientfd)
void echo(int connfd)
{
    size_t n;
    char buf[MAXLINE];
    rio_t rio;
    Rio_readinitb(&rio, connfd);
    while((n = Rio_readlineb(&rio, buf, MAXLINE)) != 0) {
        printf("server received %d bytes\n", (int)n);
Rio_writen(connfd, buf, n);
    }
}
echo.c

---
Testing Servers Using telnet
Testing Servers Using telnet
The telnet program is invaluable for testing servers that transmit ASCII strings over Internet connections
  - Our simple echo server
  - Web servers
  - Mail servers
- Usage:
  - linux> telnet <host> <portnumber>
  - Creates a connection with a server running on <host> and listening on port <portnumber>

---
Testing the Echo Server With telnet
Testing the Echo Server With telnet
whaleshark> ./echoserveri 15213
Connected to (MAKOSHARK.ICS.CS.CMU.EDU, 50280)
server received 11 bytes
server received 8 bytes
makoshark> telnet whaleshark.ics.cs.cmu.edu 15213
Trying 128.2.210.175...
Connected to whaleshark.ics.cs.cmu.edu (128.2.210.175).
Escape character is '^]'.
Hi there!
Hi there!
Howdy!
Howdy!
^]
telnet> quit
Connection closed.
makoshark>

---
Summary
Sockets used to communicate across processes over a network (even same network card)
  - TCP sockets – Listening vs connecting sockets
  - Quirks in structs representing network addresses.
  - Use getaddrinfo() or fill up the struct yourself.
  - Usage of rio library for buffered I/O.

---
Iterative Servers
Iterative Servers
Iterative servers process one request at a time
Client 1
Server
Client 2
connect
connect
accept
read
write
write
call read
call read
write
ret read
read
close
Wait for server to finish with Client 1
close
accept
read
write
ret read

---
Where Does Second Client Block?
Where Does Second Client Block?
Second client attempts to connect to iterative server
Call to connect returns
  - Even though connection not yet accepted
  - Server side TCP manager queues request
  - Feature known as “TCP listen backlog”
- Call to rio_writen returns
  - Server side TCP manager buffers input data
- Call to rio_readlineb blocks
  - Server hasn’t written anything for it to read yet.
Client
socket
rio_readlineb
rio_writen
Connection
request
open_clientfd
connect

---
Fundamental Flaw of Iterative Servers
Fundamental Flaw of Iterative Servers
Client 1
Server
Client 2
connect
connect
accept
call read
write
write
call read
call read
write
ret read
call read
Client 2 blocks
waiting to read
from server
User goes
out to lunch
Client 1 blocks
waiting for user
to type in data
Server blocks
waiting for
data from
Client 1
Solution: use concurrent servers instead
  - Concurrent servers use multiple concurrent flows to serve multiple clients at the same time

---
Approaches for Writing Concurrent Servers
Approaches for Writing Concurrent Servers
Allow server to handle multiple clients concurrently
1. Process-based
  1. Kernel automatically interleaves multiple logical flows
  2. Each flow has its own private address space
2. Event-based
  1. Programmer manually interleaves multiple logical flows
  2. All flows share the same address space
  3. Uses technique called I/O multiplexing.
3. Thread-based
  1. Kernel automatically interleaves multiple logical flows
  2. Each flow shares the same address space
  3. Hybrid of of process-based and event-based.

---
Approach #1: Process-based Servers
Approach #1: Process-based Servers
Spawn separate process for each client
client 1
server
client 2
call accept
call connect
ret accept
call connect
call fgets
fork
child 1
User goes out to lunch
Client 1 blocks
waiting for user to type in data
call accept
call read
ret accept
Child blocks waiting for data from Client 1
call fgets
fork
write
child 2
call read
call
read
...
write
ret read
close
close

---
Process-Based Concurrent Echo Server
Process-Based Concurrent Echo Server
int main(int argc, char **argv)
{
    int listenfd, connfd;
    socklen_t clientlen;
    struct sockaddr_storage clientaddr;
    Signal(SIGCHLD, sigchld_handler);
    listenfd = Open_listenfd(argv[1]);
    while (1) {
        clientlen = sizeof(struct sockaddr_storage);
        connfd = Accept(listenfd, (SA *) &clientaddr, &clientlen);
        if (Fork() == 0) {
        Close(listenfd); /* Child closes its listening socket */
        echo(connfd); /* Child services client */
        Close(connfd); /* Child closes connection with client */
        exit(0); /* Child exits */
        }
        Close(connfd); /* Parent closes connected socket (important!) */
    }
}
echoserverp.c

---
Process-Based Concurrent Echo Server
(cont)
Process-Based Concurrent Echo Server (cont)
void sigchld_handler(int sig)
{
    while (waitpid(-1, 0, WNOHANG) > 0)
        ;
    return;
}
echoserverp.c
  - Reap all zombie children

---
Issues with Process-based Servers
Issues with Process-based Servers
Listening server process must reap zombie children
  - to avoid fatal memory leak
- Parent process must close its copy of connfd
  - Kernel keeps reference count for each socket/open file
  - After fork, refcnt(connfd) = 2
  - Connection will not be closed until refcnt(connfd) = 0

---
Pros and Cons of Process-based Servers
Pros and Cons of Process-based Servers
- + Handle multiple connections concurrently
- + Clean sharing model
  - descriptors (no)
  - file tables (yes)
  - global variables (no)
- + Simple and straightforward
- – Additional overhead for process control
- – Nontrivial to share data between processes
  - Requires IPC (interprocess communication) mechanisms
    - FIFO’s (named pipes), System V shared memory and semaphores

---
Approach #2: Event-based Servers
Approach #2: Event-based Servers
Server maintains set of active connections
  - Array of connfd’s
- Repeat:
  - Determine which descriptors (connfd’s or listenfd) have pending inputs
    - e.g., using select or epoll functions
    - arrival of pending input is an event
  - If listenfd has input, then accept connection
    - and add new connfd to array
  - Service all connfd’s with pending inputs
Details for select-based server in book

---
Pros and Cons of Event-based Servers
Pros and Cons of Event-based Servers
- + One logical control flow and address space.
- + Can single-step with a debugger.
- + No process or thread control overhead.
  - Design of choice for high-performance Web servers and search engines. e.g., Node.js, nginx, Tornado
- – Significantly more complex to code than process- or thread-based designs.
- – Hard to provide fine-grained concurrency
  - E.g., how to deal with partial HTTP request headers
- – Cannot take advantage of multi-core
  - Single thread of control

---
Approach #3: Thread-based Servers
Approach #3: Thread-based Servers
Very similar to approach #1 (process-based)
  - …but using threads instead of processes

---
Threads vs. Processes
Threads vs. Processes
How threads and processes are similar
  - Each has its own logical control flow
  - Each can run concurrently with others (possibly on different cores)
  - Each is context switched
- How threads and processes are different
  - Threads share all code and data (except local stacks)
    - Processes (typically) do not
  - Threads are somewhat less expensive than processes
    - Process control (creating and reaping) twice as expensive as thread control
    - Linux numbers:
      - ~20K cycles to create and reap a process
      - ~10K cycles (or less) to create and reap a thread

---
Posix Threads (Pthreads) Interface
Posix Threads (Pthreads) Interface
Pthreads: Standard interface for ~60 functions that manipulate threads from C programs
  - Creating and reaping threads
    - pthread_create()
    - pthread_join()
  - Determining your thread ID
    - pthread_self()
  - Terminating threads
    - pthread_cancel()
    - pthread_exit()
    - exit() [terminates all threads] , RET [terminates current thread]
  - Synchronizing access to shared variables
    - pthread_mutex_init
    - pthread_mutex_[un]lock

---
Thread-Based Concurrent Echo Server
Thread-Based Concurrent Echo Server
int main(int argc, char **argv)
{
    int listenfd, *connfdp;
    socklen_t clientlen;
    struct sockaddr_storage clientaddr;
    pthread_t tid;
    listenfd = Open_listenfd(argv[1]);
    while (1) {
clientlen=sizeof(struct sockaddr_storage);
connfdp = Malloc(sizeof(int));
*connfdp = Accept(listenfd,
        (SA *) &clientaddr, &clientlen);
Pthread_create(&tid, NULL, thread, connfdp);
    }
}
echoservert.c
malloc of connected descriptor necessary to avoid deadly race

---
Thread-Based Concurrent Server (cont)
Thread-Based Concurrent Server (cont)
/* Thread routine */
void *thread(void *vargp)
{
    int connfd = *((int *)vargp);
    Pthread_detach(pthread_self());
    Free(vargp);
    echo(connfd);
    Close(connfd);
    return NULL;
}
echoservert.c
  - Run thread in “detached” mode.
    - Runs independently of other threads
    - Reaped automatically (by kernel) when it terminates
  - Free storage allocated to hold connfd.
  - Close connfd (important!)

---
Thread-based Server Execution Model
Thread-based Server Execution Model
Connection requests
Listening
server
main thread
Client 1
server
peer
thread
Client 2
server
peer
thread
Client 1 data
Client 2 data
  - Each client handled by individual peer thread
  - Threads share all process state except TID
  - Each thread has a separate stack for local variables

---
Pre-threaded Server Model
Pool of worker threads
Service client
Client
Worker
thread
Insert
descriptors
Master
thread
Accept
connections
Remove
descriptors
Buffer
...
...
Client
Worker
thread
Service client
  - Clients handled using a thread-pool architecture
  - Bounded/Unbounded buffer can be used for synchronization

---
Pros and Cons of Thread-Based Designs
Pros and Cons of Thread-Based Designs
+ Easy to share data structures between threads
  - e.g., logging information, file cache
- + Threads are more efficient than processes
- – Unintentional sharing can introduce subtle and hard-to-reproduce errors!
  - The ease with which data can be shared is both the greatest strength and the greatest weakness of threads
  - Hard to know which data shared & which private
  - Hard to detect by testing
    - Probability of bad race outcome very low
    - But nonzero!

---
Summary: Approaches to Concurrency
Summary: Approaches to Concurrency
Process-based
  - Hard to share resources: Easy to avoid unintended sharing
  - High overhead in adding/removing clients
- Event-based
  - Tedious and low level
  - Total control over scheduling
  - Very low overhead
  - Cannot create as fine grained a level of concurrency
  - Does not make use of multi-core
- Thread-based
  - Easy to share resources: Perhaps too easy
  - Medium overhead
  - Not much control over scheduling policies
  - Difficult to debug
    - Event orderings not repeatable

---
Code references can be found at
http://csapp.cs.cmu.edu/3e/code.html

---
Intro to A3 and A4
- A3 handed out today, due on 21/11 at 16:00
- A4 handed out 22/11, due on 05/12 at 16:00
- Same format as before, some programming plus a report
- Both are linked, you will build your answer to A4 on A3
- This is a large system, with some aspects you will not (yet) understand

---
Peer to Peer Network
Tracker
- P2P is a way to share data files
- Peers connect to a network by
  registering with a tracker server
- Peers can get a list of all registered
  peers from the tracker (This also
  enrols them in the network)
- Peers can download locally missing
  data from other peers, or provide
  locally available data to others
Internet
D
D
Peers

---
Cascade Files
- Each data file has a cascade file assosiated
  with it, used to track what contents a data
  file should contain
- Data files are divided into chunks,
  with a hash taken of each chunk.
  This is a way of checking what the
  data contains, without replicating
  all of the data.
- A peer can read a cascade file, and
  determine if the expected data is
  locally present.
Tracker
Internet
D
C
D
C
D
D
Peers
C

---
A3
- For A3 you need to implement the
  first half of the peer
- Your peer should parse a cascade
  file, connect to the tracker, and
  retrieve missing data from other
  peers
- A skeleton (cascade.c) has been
  provided
- Python implementations of both the
  peer and tracker have been provided
Tracker
Internet
D
C
D
C
D
D
Peers
C
D

---
A4
- For A3 you will implement the
  second half
- Your peer should also be able to
  act as a source for other peers,
  once the data is available locally
- Your peer should be capable of
  accepting multiple inputs at once
- You can complete A3 in isolation,
  but may also wish to keep A4 in
  mind during A3
Tracker
Internet
D
C
D
D
C
D
D
Peers
C
D